## Slide 1
Three Instruction Word Formats
Register Format (R-Format)
Instruction fields
  op: operation code (opcode)
  rs: first source register number
  rt: second source register number
  rd: destination register number
  shamt: shift amount (00000 for now)
  funct: function code (extends opcode)
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits

## Slide 2
Three Instruction Word Formats
Immediate Format (I-Format)
Op-Code Rs Rt 16 - Bit Immediate Value
6 5 5 16
Immediate arithmetic and load/store instructions
  rt: destination or source register number
  Constant: –215 to +215 – 1
  Address: offset added to base address in rs

## Slide 3
Three Instruction Word Formats
Jump Format (J-Format)
Op-Code 26 Bit Current Segment Address
6 26
jump instruction;
j 10000; go to target address 10000
jal 10000; $31 = PC + 4; go to 10000; for procedure call,
; return address is saved in $31

## Slide 4
Convert the following to Machine Code:
Sub $t0,$s4,$s5
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
Go and check MIPS reference Data

## Slide 5
Go and check MIPS reference Data

## Slide 6
Next, we need to determine the registers numbers

## Slide 7
0x29540022

## Slide 8
How to convert MIPS Assembly to Machine language.
Convert the following instruction into a machine language:
Slti $t1, $a0, 0xf8
Op-Code Rs Rt 16 - Bit Immediate Value
6 5 5 16
Immediate arithmetic and load/store instructions
  rt: destination or source register number
  Constant: –215 to +215 – 1
  Address: offset added to base address in rs
https://courses.cs.washington.edu/courses/cse378/09au/MIPS_Green_Sheet.pdf

## Slide 9
0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0
How to convert MIPS Assembly to Machine language.
Convert the following instruction into a machine language:
Slti $t1, $a0, 0xf8
Op-Code
6
Rs
5
Rt
5
16 - Bit Immediate Value
  t1: destination
  a0: Source
f
8
a
$t1
a0
0x288900f8
0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0
8
8
8
9
0
0
f
2
Hexadecimal representation

## Slide 11
Convert the following Machine Code to MIPS Instructions
0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0
Slti $t1, $a0, 0xf8